## Slide 1: Mobile Communication Unit – 1 Introduction
By
Ms.A.Thamizhiniyal, M.C.A., M.Phil.,
Assistant Professor,
Bon Secours College for Women, Thanjavur

## Slide 2: Definition
Mobile communications refers to a form of communications which does not depend on a physical connection between the sender and receiver and who may move from one physical location to another during communication
Mobile computing means different things to different peoples. Ubiqutious wireless and remote computing Wireless is a transmission or information transport method that enables mobile computing.
Aspects of Mobility
User Mobility
  User Communicates anytime, anywhere, with anyone
Device Portability
  Devices can be connected anytime, anywhere to the network

## Slide 3: Applications
        Vehicles
        Emergencies
        Travelling Salesman
        Replacement of fixed networks
        Entertainment
        Education

## Slide 4: Simplified Reference Model

## Slide 5: Reference Model
Physical Layer
 Bit Stream to signal conversion
 Frequency selection
 Generation of carrier frequency
 Data modulation over carrier frequency
 Data encryption
Data Link Layer
 Data Multiplexing
 Error detection and correction
 Medium Access

## Slide 6
Network Layer
 Connection setup
 Packet routing
 Handover between networks
 Routing
 Target device location
 Quality of service (QoS)
Transport Layer
 Establish End-to-End Connection
 Flow control
 Congestion control
 TCP and UDP
 Applications – Browser etc.

## Slide 7
Application Layer
 Multimedia applications
 Applications that interface to various kinds of data formats and transmission characteristics
 Applications that interface to various portable devices

## Slide 8: Wireless Transmission
Frequencies
Signals
Antennas
Signal propagation
Multiplexing
Spread spectrum
Modulation
Cellular systems

## Slide 9: Spectrum Allocation
VLF = Very Low Frequency UHF = Ultra High Frequency
LF = Low Frequency SHF = Super High Frequency
MF = Medium Frequency EHF = Extra High Frequency
HF = High Frequency UV = Ultraviolet Light
VHF = Very High Frequency
Relationship between frequency ‘f’ and wave length ‘’ :
 = c/f
where c is the speed of light  3x108m/s
1 Mm
300 Hz
10 km
30 kHz
100 m
3 MHz
1 m
300 MHz
10 mm
30 GHz
100 m
3 THz
1 m
300 THz
visible light
VLF
LF
MF
HF
VHF
UHF
SHF
EHF
infrared
UV
optical transmission
coax cable
twisted pair

## Slide 10: Frequencies Allocated for Mobile Communication
VHF & UHF ranges for mobile radio
  allows for simple, small antennas for cars
  deterministic propagation characteristics
  less subject to weather conditions –> more reliable connections
SHF and higher for directed radio links, satellite communication
  small antennas with directed transmission
  large bandwidths available
Wireless LANs use frequencies in UHF to SHF spectrum
  some systems planned up to EHF
  limitations due to absorption by water and oxygen molecules
    weather dependent fading, signal loss caused by heavy rainfall, etc.

## Slide 11: Allocated Frequencies
ITU-R holds auctions for new frequencies, manages frequency bands worldwide for harmonious usage (WRC - World Radio Conferences)

## Slide 12: Signals I
physical representation of data
function of time and location
signal parameters: parameters representing the value of data
classification
  continuous time/discrete time
  continuous values/discrete values
  analog signal = continuous time and continuous values
  digital signal = discrete time and discrete values
signal parameters of periodic signals: period T, frequency f=1/T, amplitude A, phase shift 
  sine wave as special periodic signal for a carrier: s(t) = At sin(2  ft t + t)

## Slide 13: Fourier Representation of Periodic Signals
1
0
1
0
t
t
ideal periodic signal
real composition
(based on harmonics)

## Slide 14: Signals II
Different representations of signals
  amplitude (amplitude domain)
  frequency spectrum (frequency domain)
  phase state diagram (amplitude M and phase  in polar coordinates)
Composite signals mapped into frequency domain using Fourier transformation
Digital signals need
  infinite frequencies for perfect representation
  modulation with a carrier frequency for transmission (->analog signal!)
f [Hz]
A [V]

I= M cos 
Q = M sin 

A [V]
t[s]

## Slide 15: Antennas
Antennas are used to radiate and receive EM waves (energy)
Antennas link this energy between the ether and a device such as a transmission line (e.g., coaxial cable)
Antennas consist of one or several radiating elements through which an electric current circulates
Types of antennas:
  omnidirectional
  directional
  phased arrays
  adaptive
  optimal
Principal characteristics used to characterize an antenna are:
  radiation pattern
  directivity
  gain
  efficiency

## Slide 16: Isotropic Antennas
Isotropic radiator: equal radiation in all directions (three dimensional) - only a theoretical reference antenna
Real antennas always have directive effects (vertical and/or horizontal)
Radiation pattern: measurement of radiation around an antenna
z
y
x
ideal
isotropic
radiator

## Slide 17: Omnidirectional Antennas: simple dipoles
Real antennas are not isotropic radiators but, e.g., dipoles with lengths /4, or Hertzian dipole: /2 (2 dipoles)  shape/size of antenna proportional to wavelength
Example: Radiation pattern of a simple Hertzian dipole
Gain: ratio of the maximum power in the direction of the main lobe to the power of an isotropic radiator (with the same average power)
side view (xy-plane)
x
y
side view (yz-plane)
z
y
top view (xz-plane)
x
z
simple
dipole
/4
/2

## Slide 18: Directional Antennas
side view (xy-plane)
x
y
side view (yz-plane)
z
y
top view (xz-plane)
x
z
top view, 3 sector
x
z
top view, 6 sector
x
z
Often used for microwave connections (directed point to point transmission) or base stations for mobile phones (e.g., radio coverage of a valley or sectors for frequency reuse)
directed
antenna
sectorized
antenna

## Slide 19: Array Antennas
Grouping of 2 or more antennas to obtain radiating characteristics that cannot be obtained from a single element
Antenna diversity
  switched diversity, selection diversity
    receiver chooses antenna with largest output
  diversity combining
    combine output power to produce gain
    cophasing needed to avoid cancellation
ground plane
+
/4
/2
/4
/2
/2
/2
+

## Slide 20: Signal Propagation Ranges
distance
sender
transmission
detection
interference
Transmission range
  communication possible
  low error rate
Detection range
  detection of the signal possible
  no communication possible, high error rate
Interference range
  signal may not be detected
  signal adds to the background noise

## Slide 21: Signal Propagation I
Radio wave propagation is affected by the following mechanisms:
  reflection at large obstacles
  scattering at small obstacles
  diffraction at edges
reflection
scattering
diffraction

## Slide 22: Signal Propagation II
The signal is also subject to degradation resulting from propagation in the mobile radio environment. The principal phenomena are:
  pathloss due to distance covered by radio signal (frequency dependent, less at low frequencies)
  fading (frequency dependent, related to multipath propagation)
  shadowing induced by obstacles in the path between the transmitted and the receiver
shadowing

## Slide 23: Signal Propagation III
Interference from other sources and noise will also impact signal behavior:
  co-channel (mobile users in adjacent cells using same frequency) and adjacent (mobile users using frequencies adjacent to transmission/reception frequency) channel interference
  ambient noise from the radio transmitter components or other electronic devices,
Propagation characteristics differ with the environment through and over which radio waves travel. Several types of environments can be identified (dense urban, urban, suburban and rural) and are classified according to the following parameters:
  terrain morphology
  vegetation density
  buildings: density and height
  open areas
  water surfaces

## Slide 24: Multipath Propagation I
Signal can take many different paths between sender and receiver due to reflection, scattering, diffraction
Positive effects of multipath:
  enables communication even when transmitter and receiver are not in LOS conditions - allows radio waves effectively to go through obstacles by getting around them thereby increasing the radio coverage area
signal at sender
signal at receiver

## Slide 25: Multipath Propagation II
Negative effects of multipath:
  Time dispersion or delay spread: signal is dispersed over time due signals coming over different paths of different lengths
   Causes interference with “neighboring” symbols, this is referred to as Inter Symbol Interference (ISI)
  multipath spread (in secs) = (longest1 – shortest2)/c
  For a 5ms symbol duration a 1ms delay spread means about a 20% intersymbol overlap.
  The signal reaches a receiver directly and phase shifted (due to reflections)
   Distorted signal depending on the phases of the different parts, this is referred to as Rayleigh fading, due to the distribution of the fades. It creates fast fluctuations of the received signal (fast fading).
  Random frequency modulation due to Doppler shifts on the different paths. Doppler shift is caused by the relative velocity of the receiver to the transmitter, leads to a frequency variation of the received signal.

## Slide 26: Effects of Mobility
Channel characteristics change over time and location
  signal paths change
  different delay variations of different signal parts
  different phases of signal parts
 quick changes in the power received (short term fading)
Additional changes in
  distance to sender
  obstacles further away
 slow changes in the average power received (long term fading)
short term fading
long term
fading
t
power

## Slide 27: Multiplexing Techniques
Multiplexing techniques are used to allow many users to share a common transmission resource. In our case the users are mobile and the transmission resource is the radio spectrum. Sharing a common resource requires an access mechanism that will control the multiplexing mechanism.
As in wireline systems, it is desirable to allow the simultaneous transmission of information between two users engaged in a connection. This is called duplexing.
Two types of duplexing exist:
  Frequency division duplexing (FDD), whereby two frequency channels are assigned to a connection, one channel for each direction of transmission.
  Time division duplexing (TDD), whereby two time slots (closely placed in time for duplex effect) are assigned to a connection, one slot for each direction of transmission.

## Slide 28: Multiplexing
Multiplexing in 3 dimensions
  time (t) (TDM)
  frequency (f) (FDM)
  code (c) (CDM)
Goal: multiple use of a shared medium
s2
s3
s1
f
t
c
k2
k3
k4
k5
k6
k1
f
t
c
f
t
c
channels ki

## Slide 29: Narrowband versus Wideband
These multiple access schemes can be grouped into two categories:
  Narrowband systems - the total spectrum is divided into a large number of narrow radio bands that are shared.
  Wideband systems - the total spectrum is used by each mobile unit for both directions of transmission. Only applicable for TDM and CDM.

## Slide 30: Frequency Division Multiplexing (FDM)
Separation of the whole spectrum into smaller frequency bands
A channel gets a certain band of the spectrum for the whole time – orthogonal system
Advantages:
  no dynamic coordination necessary, i.e., sync. and
  framing
  works also for analog signals
  low bit rates – cheaper,
  delay spread
Disadvantages:
  waste of bandwidth if the traffic is distributed unevenly
  inflexible
  guard bands
  narrow filters
k2
k3
k4
k5
k6
k1
f
t
c

## Slide 31: Time Division Multiplexing (TDM)
f
t
c
k2
k3
k4
k5
k6
k1
A channel gets the whole spectrum for a certain amount of time – orthogonal system
Advantages:
  only one carrier in the medium at any time
  throughput high - supports bursts
  flexible – multiple slots
  no guard bands ?!
Disadvantages:
  Framing and precise synchronization necessary
  high bit rates
  at each
  Tx/Rx

## Slide 32: Hybrid TDM/FDM
f
Combination of both methods
A channel gets a certain frequency band for a certain amount of time (slot).
Example: GSM, hops from one band to another each time slot
Advantages:
  better protection against tapping (hopping among
  frequencies)
  protection against frequency selective interference
Disadvantages:
  Framing and
  sync. required
t
c
k2
k3
k4
k5
k6
k1

## Slide 33: Code Division Multiplexing (CDM)
Each channel has a unique code
(not necessarily orthogonal)
All channels use the same spectrum at the same time
Advantages:
  bandwidth efficient
  no coordination and synchronization necessary
  good protection against interference and tapping
Disadvantages:
  lower user data rates due to high gains required to reduce interference
  more complex signal regeneration
2.19.1
k2
k3
k4
k5
k6
k1
f
t
c

## Slide 34: Issues with CDM
CDM has a soft capacity. The more users the more codes that are used. However as more codes are used the signal to interference (S/I) ratio will drop and the bit error rate (BER) will go up for all users.
CDM requires tight power control as it suffers from far-near effect. In other words, a user close to the base station transmitting with the same power as a user farther away will drown the latter’s signal. All signals must have more or less equal power at the receiver.
Rake receivers can be used to improve signal reception. Time delayed versions (a chip or more delayed) of the signal (multipath signals) can be collected and used to make bit level decisions.
Soft handoffs can be used. Mobiles can switch base stations without switching carriers. Two base stations receive the mobile signal and the mobile is receiving from two base stations (one of the rake receivers is used to listen to other signals).
Burst transmission - reduces interference

## Slide 35: Types of CDM I
Two types exist:
  Direct Sequence CDM (DS-CDM)
    spreads the narrowband user signal (Rbps) over the full spectrum by multiplying it by a very wide bandwidth signal (W). This is done by taking every bit in the user stream and replacing it with a pseudonoise (PN) code (a long bit sequence called the chip rate). The codes are orthogonal (or approx.. orthogonal).
    This results in a processing gain G = W/R (chips/bit). The higher G the better the system performance as the lower the interference. G2 indicates the number of possible codes. Not all of the codes are orthogonal.

## Slide 36: Types of CDM II
  Frequency hopping CDM (FH-CDM)
    FH-CDM is based on a narrowband FDM system in which an individual user’s transmission is spread out over a number of channels over time (the channel choice is varied in a pseudorandom fashion). If the carrier is changed every symbol then it is referred to as a fast FH system, if it is changed every few symbols it is a slow FH system.

## Slide 37: Modulation
Digital modulation
  digital data is translated into an analog signal (baseband)
  ASK, FSK, PSK - main focus in this chapter
  differences in spectral efficiency, power efficiency, robustness
Analog modulation
  shifts center frequency of baseband signal up to the radio carrier
Motivation
  smaller antennas (e.g., /4)
  Frequency Division Multiplexing
  medium characteristics
Basic schemes
  Amplitude Modulation (AM)
  Frequency Modulation (FM)
  Phase Modulation (PM)

## Slide 38: Modulation and Demodulation
synchronization
decision
digital
data
analog
demodulation
radio
carrier
analog
baseband
signal
101101001
radio receiver
digital
modulation
digital
data
analog
modulation
radio
carrier
analog
baseband
signal
101101001
radio transmitter

## Slide 39: Digital Modulation
Modulation of digital signals known as Shift Keying
Amplitude Shift Keying (ASK):
  very simple
  low bandwidth requirements
  very susceptible to interference
Frequency Shift Keying (FSK):
  needs larger bandwidth
Phase Shift Keying (PSK):
  more complex
  robust against interference
1
0
1
t
1
0
1
t
1
0
1
t

## Slide 40: Spread spectrum technology: CDM
Problem of radio transmission: frequency dependent fading can wipe out narrow band signals for duration of the interference
Solution: spread the narrow band signal into a broad band signal using a special code
  protection against narrow band interference
protection against narrowband interference
Side effects:
  coexistence of several signals without dynamic coordination
  tap-proof
Alternatives: Direct Sequence, Frequency Hopping
detection at
receiver
interference
spread signal
signal
spread
interference
f
f
power
power

## Slide 41: Effects of spreading and interference
P
f
i)
P
f
ii)
sender
P
f
iii)
P
f
iv)
receiver
f
v)
user signal
broadband interference
narrowband interference
P

## Slide 42: Spreading and frequency selective fading
frequency
channel quality
1
2
3
4
5
6
narrow band signal
guard space
2
2
2
2
2
frequency
channel quality
1
spread spectrum
narrowband channels
spread spectrum channels

## Slide 43: DSSS (Direct Sequence Spread Spectrum) I
XOR of the signal with pseudo-random number (chipping sequence)
  many chips per bit (e.g., 128) result in higher bandwidth of the signal
Advantages
  reduces frequency selective fading
  in cellular networks
    base stations can use the same frequency range
    several base stations can detect and recover the signal
    soft handover
Disadvantages
  precise power control necessary
user data
chipping
sequence
resulting
signal
0
1
0
1
1
0
1
0
1
0
1
0
0
1
1
1
XOR
0
1
1
0
0
1
0
1
1
0
1
0
0
1
=
tb
tc
tb: bit period
tc: chip period

## Slide 44: DSSS (Direct Sequence Spread Spectrum) II
X
user data
chipping
sequence
modulator
radio
carrier
spread
spectrum
signal
transmit
signal
transmitter
demodulator
received
signal
radio
carrier
X
chipping
sequence
lowpass
filtered
signal
receiver
integrator
products
decision
data
sampled
sums
correlator

## Slide 45: FHSS (Frequency Hopping Spread Spectrum) I
Discrete changes of carrier frequency
  sequence of frequency changes determined via pseudo random number sequence
Two versions
  Fast Hopping: several frequencies per user bit
  Slow Hopping: several user bits per frequency
Advantages
  frequency selective fading and interference limited to short period
  simple implementation
  uses only small portion of spectrum at any time
Disadvantages
  not as robust as DSSS
  simpler to detect

## Slide 46: FHSS (Frequency Hopping Spread Spectrum) II
user data
slow
hopping
(3 bits/hop)
fast
hopping
(3 hops/bit)
0
1
tb
0
1
1
t
f
f1
f2
f3
t
td
f
f1
f2
f3
t
td
tb: bit period td: dwell time

## Slide 47: FHSS (Frequency Hopping Spread Spectrum) III
modulator
user data
hopping
sequence
modulator
narrowband
signal
spread
transmit
signal
transmitter
received
signal
receiver
demodulator
data
frequency
synthesizer
hopping
sequence
demodulator
frequency
synthesizer
narrowband
signal
2.34.1

## Slide 48: Concept of Cellular Communications
In the late 60’s it was proposed to alleviate the problem of spectrum congestion by restructuring the coverage area of mobile radio systems.
The cellular concept does not use broadcasting over large areas. Instead smaller areas called cells are handled by less powerful base stations that use less power for transmission. Now the available spectrum can be re-used from one cell to another thereby increasing the capacity of the system.
However this did give rise to a new problem, as a mobile unit moved it could potentially leave the coverage area (cell) of a base station in which it established the call. This required complex controls that enabled the handing over of a connection (called handoff) to the new cell that the mobile unit moved into.
In summary, the essential elements of a cellular system are:
  Low power transmitter and small coverage areas called cells
  Spectrum (frequency) re-use
  Handoff

## Slide 49: Cell structure
Implements space division multiplex: base station covers a certain transmission area (cell)
Mobile stations communicate only via the base station
Advantages of cell structures:
  higher capacity, higher number of users
  less transmission power needed
  more robust, decentralized
  base station deals with interference, transmission area etc. locally
Problems:
  fixed network needed for the base stations
  handover (changing from one cell to another) necessary
  interference with other cells
Cell sizes from some 100 m in cities to, e.g., 35 km on the country side (GSM) - even less for higher frequencies

## Slide 50: Cellular Network

## Slide 51: Definitions
Forward path or down link - from base station down to the mobile
Reverse path or up link - from the mobile up to the base station
The mobile unit - a portable voice and/or data comm. transceiver. It has a 10 digit telephone number that is represented by a 34 bit mobile identification number -> (215) 684-3201 is divided into two parts: MIN1: 215 translated into 10bits and MIN2: 684-3201 translated into 24bits. In addition each mobile unit is also permanently programmed at the factory with a 32 bit electronic serial number (ESN) which guards against tampering.
The cell - a geographical area covered by Radio Frequency (RF) signals. It is essentially a radio communication center comprising radios, antennas and supporting equipment to enable mobile to land and land to mobile communication. Its shape and size depend on the location, height , gain and directivity of the antenna, the power of the transmitter, the terrain, obstacles such as foliage, buildings, propagation paths, etc. It is a highly irregular shape, its boundaries defined by received signal strength! But for traffic engineering purposes and system planning and design a hexagonal shape is used.

## Slide 52: Definitions
The base station (BS) - a transmitter and receiver that relays signals (control and information (voice or data)) from the mobile unit to the MSC and vice versa.
The mobile switching center (MSC) - a switching center that controls a cluster of cells. Base stations are connected to the MSC via wireline links. The MSC is directly connected to the PSTN and is responsible for all calls related to mobiles located within its domain. MSCs intercommunicate using a link protocol specified by IS (International Standard) 41. This enables roaming of mobile units (i.e. obtaining service outside of the home base). The MSC is also responsible for billing, it keeps track of air time, errors, delays, blocking, call dropping (due to handoff failure), etc. It is also responsible for the handoff process, it keeps track of signal strengths and will initiate a handoff when deemed necessary (note to handoff or not to handoff is not a trivial issue!)

## Slide 53: Spectrum and Capacity Issues
Spectrum is limited

## Slide 54: Frequency planning
Frequency reuse only with a certain distance between the base stations
Standard model using 7 frequencies:
Fixed frequency assignment:
  certain frequencies are assigned to a certain cell
  problem: different traffic load in different cells
Dynamic frequency assignment:
  base station chooses frequencies depending on the frequencies already used in neighbor cells
  more capacity in cells with more traffic
  assignment can also be based on interference measurements
f4
f5
f1
f3
f2
f6
f7
f3
f2
f4
f5
f1

## Slide 55: Increasing Capacity
We can see that by reducing the area of a cell we can increase capacity as we will have more cells each with its own set of frequencies.
What is drawback of shrinking the size of the cells (cell splitting)? Increase in the number of handoffs -> increased load on the system! Also need more infrastrucutre -> base stations (each cell needs a BS).
An easier solution exists, sectorization. It does not reduce handoffs, its advantage: it does not require more infrastructure.

## Slide 56: MAC – Medium Access Protocol
 Schedule-based: Establish transmission schedules statically or dynamically o TDMA o FDMA o CDMA
 Contention-based: o Let the stations contend for the channel o Random access protocols
 Reservation-based: o Reservations made during a contention phase o Size of packet in contention phase much smaller than a data packet
 Space-division multiple access: o Serve multiple users simultaneously by using directional antennas