## Slide 1: HAEMODIALYSIS
M. KARTHIKA
Asst Professor,
Dept of Physics,
Bon Secours College for Women , Thanjavur Dt.

## Slide 2
WHAT IS DIALYSIS?
A medical procedure to remove fluid and waste products from the blood and to correct electrolyte imbalances.
This is accomplished using a machine and a dialyzer, also referred to as an "artificial kidney."
Hemodialysis is used to treat both acute (temporary) and chronic (permanent) kidney failure.

## Slide 3: WHEN WE NEED DIALYSIS?
CHRONIC RENAL FAILURE- FULLY DAMAGE
ACUTE RENAL FAILURE- DAMAGED BY DISEASE
CHRONIC
FULLY DAMAGED
NEED KIDNEY TRANSPLANT
ACUTE
DISEASE
ACCIDENT

## Slide 4: TYPES OF DIALYSIS
PERITIONATE DIALYSIS
HAEMODIALYSIS

## Slide 5
The kidneys are a perfect filter which perform the function of removal of waste products through the urine.
BASICS OF KIDNEY FUNCTION

## Slide 6: FUNCTION OF THE NORMAL KIDNEY
BEAN SHAPED
12 CM LONG; 150G WEIGHT
MILLIONS OF NEPRONS
GLOMERULUS & TUBULE
PLASMA ----- GLOMERULLI ------ CAPILLARY LOOP (PASSIVE PROCESS)
60 TIMES PER DAY – URINE OUTPUT- ACTIVE PROCESS
ENERGY REQUIRED FOR ACTIVE PROCESS

## Slide 7: CONCENTRATION OF ELECTROLYTES
ELECTROLYTES | CONCENTRATION mmol
SODIUM | 132-142
CHLORIDE | 100
BICARBONATE | 25
POTASSIUM | 3.9-5.0
CALCIUM | 2.5

## Slide 8
Sometimes, when the kidneys get infected and do not function properly, the person starts suffering which can lead to his/her death.
Such people are put on to artificial kidneys, also known as dialyser.
Dialyser is a machine that filters the blood of harmful substances.
Blood from a blood vessel is drawn into the dialyser and then purified to be fed into another blood vessel of the body.
Such people have to be dialysed after every 2-3 days.
Damaged kidneys are also replaced either from a donor or a dead person.
DIALYSER?????

## Slide 9: HISTORY OF DIALYSIS

## Slide 10: TYPES OF DIALYSER
PARALLEL PLATE – BLOOD FLOWS BETWEEN PARALLEL SHEETS OF MEMBRANE-65-86mL
HOLLOW FIBRE- BLOODS FLOWS THROUGH HOLLOW FIBERS – 70-100mL

## Slide 11: DIALYZER MEMBRANE
Cellulose:
Obtained form processed cotton (regenerated cellulose, cuprammonium cellulose, cuprammonium rayon and saponified cellulose)
Substituted cellulose:
Cellulose polymer has a large number of free hydroxyl group at its surface
Free hydroxyl group are responsible for blood cell activation causing bio-incompatibiltiy of the dialyzer (cellulose acetate, cellulose diacetate, triacetate)
Synthetic material e.g(polyacrylorinate, polysulfone)

## Slide 12: PRINCIPLES OF HAEMODIALYSIS
Dialysis works on the principles of the diffusion of solutes and ultrafiltration of fluid across a semi-permeable membrane.
Diffusion is a property of substances in water substances in water tend to move from an area of high concentration to an area of low concentration.

## Slide 13: DIFFUSION
10-20 Micrometer thickness
Pores about 500nm
>5000 – pass easily
(5000- 40000)- pass slowly
Remove amino acids, some drugs

## Slide 14: OSMOSIS
A process by which molecules of a solvent tend to pass through a semipermeable membrane from a less concentrated solution into a more concentrated one.

## Slide 15: ULTRAFILTRATION
The movement of water across a membrane as a result of hydrostatic pressure is called Ultrafiltration.

## Slide 16: Working of dialysis machine

## Slide 17: Importance of Dialysis
The dialysis fluid
Mixing of dialysis fluid
Dialysate temperature
Blood leak detector
The extracorporeal blood circuit
Access of circulation

## Slide 18
THANK YOU