## Slide 1: Pattern making
M.ROCH SOUMIA
ASSISTANT PROFESSOR
DEPT OF FASHION TECHNOLOGY & COSTUME DESIGNING
SHRIMATI INDIRA GANDHI COLLEGE, TRICHY.

## Slide 2: What is a pattern?
Paper pieces
Communicates shapes of fabric pieces to cut to make a garment in a specific style and size
Communicates markings needed to construct the garment

## Slide 3: Types of Patternmaking
How are patterns made?
  Knock-off
    Tracing the pattern pieces from an existing garment
  Draping
    Using fabric on a dress form to create pattern shapes, which are transferred to paper.
  Pattern drafting:
    Using measurements taken from a form or model to create sloper patterns.
    Sloper (“working pattern”): Any pattern used as a base for manipulation when generating design patterns. It is developed without design features.
  Flat patternmaking:
    Manipulating previously developed sloper patterns to create design patterns.

## Slide 4: Dart Terminology
Dart:
  A wedge-shaped cutout in a pattern to control the fit of a garment.
Bust point:
  A designated place on the bust and pattern and referred to in flat patternmaking as the pivotal point or apex.
Dart intake:
  The amount of excess (or space) confined between dart legs.
  Its purposes are to take up excess where it is not needed, and to gradually release fabric where it is needed to control the fit of the garment.
Dart legs:
  The two lines that converge at a predetermined point on the pattern.

## Slide 5: Function of Patternmaking Tools
Create pattern lines and curves
Mark symbols
  Communicate important information so garment will be cut and stitched accurately
  Throughout flow of production

## Slide 6: Function of Patternmaking Tools
Seamstress
Grader
Marker Maker
Designer
Patternmaker

## Slide 7: Patternmaking Tools
Clear plastic grid ruler
18” X 2”
Tailor's square (L-square):
  Metal
  two arms forming a 90° angle that measures, rules, and squares simultaneously.

## Slide 8: Patternmaking Tools - Required
French curve:
  ideal for shaping armholes and necklines
Vary form curve:
  blends and shapes armholes, necklines, and other curves

## Slide 9: Patternmaking Tools
Pattern snips
Awl:
  A sharp pointed tool that pierces a 1/8 inch hole in patterns.

## Slide 10: Patternmaking Tools
Tracing wheels:
  Pointed and blunted wheels that transfer pattern shapes to paper.

## Slide 11: Patternmaking Tools—Paper
Pattern paper
  Light weight
  Used for first patterns
Tag board
  Used for slopers and production patterns

## Slide 12: Patternmaking Tools—Muslin
A plain-woven cotton made from bleached or unbleached corded yarns in a variety of weights:
  Coarse-weave:
    Used for draping and testing basic patterns;
  Light-weight:
    Used for softly draped garments;
  Heavy-weight:
    Firmly woven, used for testing tailored garments, jackets, and coats.

## Slide 13: The Important Grain line
Grain:
  The direction in which the yarn is woven or knitted.
Crosswise grain :
  Yarns woven across the fabric from selvage to selvage.
  Crosswise grain yields to tension.
Lengthwise grain:
  Yarns parallel with selvage.
  It is the most stable grain.
Selvage:
  The narrow, firmly woven, and finished strip on both lengthwise grain edges of the woven fabric.

## Slide 14: More About Grainlines
Bias:
  Any slanting or diagonal line cut or sewn across the weave of the cloth.
True bias:
  The line that intersects with the lengthwise and crosswise grains at a 45° angle.
  True bias has maximum give and stretch, easily conforming to the figure's contours.
  Flares, cowls, and drapes work best when cut on true bias.

## Slide 15: Grain lines on Patterns
A line drawn on each pattern piece
Indicates how the pattern should align with the lengthwise grain of the fabric.
  Always mark the lengthwise grain on every pattern piece!
  Grainline should extend from edge to edge
Grainline arrows:
  1. Arrows placed at both ends
    the pattern may be placed in either direction along the lengthwise grainline of the fabric (for fabrics without a nap).
  2. An arrow placed at the top or the bottom
    the pattern must be placed in one direction only (for fabrics with a nap).

## Slide 16: Patternmaking Procedures
Neat workmanship is essential.
Always draft for the right side of the body
Always draft without seam allowances.
Trueing:
  Establishing correct seam lengths—for example, trueing a side seam having a side dart.
Blending
  The smoothing and straightening of pencil lines, crossmarks, and dot marks
Walking
Balancing

## Slide 17: Guidelines for Pattern Labeling
Grainline: Mark lengthwise on every piece
  2” (or more) away from CF or CB
Pattern number - size - number to cut: along grainline
  1050 - 8 - 2
Name of pattern piece
Your name
CF and CB: center front and center back –
Fold lines: dotted line . . . . . . . . . .
Gathers: dashed line ------------
Buttonhole [--------] and button x
Dart points - punch hole ½” inside apex and circle
Thumbnail sketch - a small sketch to represent the finished garment on a main pattern piece
Fabrication - woven or knit
Right-side-up:
  Indicates to the marker maker that the pattern is to be placed face up on the marker (for asymmetrical designs).
Detail location:
  placement of flower or other detail

## Slide 18: Guidelines for Notches
Use a SINGLE NOTCH to indicate FRONT pattern pieces
Use a DOUBLE NOTCH to indicate BACK pattern pieces
Use a TRIPLE NOTCH to indicate CB and base of zipper
NOTCH
  CF and CB
  hem depth
  1" side seams
  connecting points on stylelines
  knee level
  waist level
  elbow level

## Slide 19: Guidelines for Seam Allowances
¼”
  Necklines with facings
  Armholes with facings
  Facings
  Tight curves
½”
  Major connecting seams
  Necklines with collars
  Armholes with sleeves
  Stylelines
  Narrow rolled hems
1"
  Side Seams
  Seams with Zippers
2"
  Most Tailored hems
Notch or outline ALL seam allowances (for classroom purposes)

## Slide 20: Patternmaking Process
First pattern
Production pattern
The original pattern developed for designs.
Generally made on marking paper
Requires fitting and pattern corrections.
The final corrected and error-free version.
The pattern contains every pattern piece required to complete the garment.
It is used by the grader for sizing and by the marker maker for fabric layout.
Marker
The arrangement of pattern pieces.
All pattern symbols are marked on the patterns.

## Slide 21: Cost Sheet
A complete record of each design that is used to cost the garment and establish the wholesale price.

## Slide 22: Pattern Chart
A complete record of all pattern pieces within the pattern set.
It also includes swatches and special pattern information.

## Slide 23: Specification Chart
A record of the finishing requirements for each design.
It is used by those responsible for finishing to ensure that the garment meets company standards.

## Slide 24: THANK YOU